## Slide 1: MAP583 Jeremie Dentan – Ahmed Laftit – Dan Meller

## Slide 2: Content
Introduction
First discussion: stability: modify the dataset:
  Presentation of the dataset
  Changing the probability q
  Changind the size of the dataset
Second discussion: performance: modify lap_pos_enc
  Without positional embedding
  Exponential factors
  Absolute value
  Homothety
  Increasing the dimension of the embedding

## Slide 3: Introduction
Two discussions
  Stability : train a network and test it on another dataset
  => Generate new datasets on CPUs
  Performance : modify the laplacian positional embedding (lap_pos_enc)
  => Train new networks on GPUs
Table 1: comparison of the GPU used.
Table 2: presentation of the CPU and computation time
GPU | Our experiments | Paper’s experiments
Material | 1 Nvidia Quatro 4000 8Go (~1000€) | 4 Nvidia 1080Ti 11Go (~4x1000€)
Epochs | 80 max | 1000 max
Computation time | 5h max per experiment | 24h max per experiment
Matériel CPU | Datasets created | Computation time/dataset
2 Intel Xeon E-2174 3.80GHz | 5 | 5h

## Slide 4: 1-a\ Stability: the PATTERN dataset
5 communities are generated with the same probabilities for each block
We add a 6th community with a different extra-link probability
Communities’ average size is 20
The goal is to classify the dataset and find which individuals belong to the 6th community

## Slide 5: 1-b\ Stabilité : faire varier q
When , it’s easier at first to find the different community
However, when is big, the model starts to lose accuracy.
The 20 epochs model seems to generalize better than the 80 epochs one.
q | Model 20 epochs | Model 80 epochs
0.15 | 77.0046 | 69.1981
0.25 | 93.2172 | 92.2461
0.35 (original model) | 83.2934 | 84.7762
0.45 | 52.1648 | 51.5637
0.55 | 42.0210 | 41.8587

## Slide 6: 1-c\ Stability: size of the dataset
As we could expect, the bigger the graph, the harder it is for the model
The 20 epochs model seems to generalize better than the 80 epochs one
Communities sizes | Model 20 epochs | Model 80 epochs
Uniform between 5 and 35 (original) | 83.2934 | 84.7762
Uniform between 35 and 65 | 68.4562 | 65.9456
Uniform between 65 and 95 | 39.8145 | 33.6427

## Slide 7: 2-a\ Performance – With or without embedding ?
Much faster and precise training with the embedding.
The gap is smaller and smaller with training
About 20% accuracy gap for the first epoch.

## Slide 8: 2-b\ Performance – Exponential factors
Exponential: give more weight to smaller eigenvalues :
Absolute value: increase sign symetry:

## Slide 9: 2-b\ Performance - Exponential factors
Results:

## Slide 10: 2-c\ Performance - Homothety
Homothety :
In theory: no change due to the neural network
In practice: difference since the signal is harder for the network to pick up information

## Slide 11: 2-d\ Performance - Dimension
The code of the paper uses the k=2 smallest eigenvalues of the Laplacian by default.
Better performances can be achieved with k=5 in the long run. Few changes for k>5.

## Slide 12: Thank you !